## Slide 1
Pore-scale NMR T₂ Workflow
3D CT Stack
Representative
2D Slice
Water Domain
2D FEM
M(x,t)
Decay S(t)
T₂ Spectrum
Chart: t
| 10⁻³ | 10⁻² | 10⁻¹ | 10⁰ | 10¹ | 10²
S(t) | 0.99681 | 0.96851 | 0.72615 | 0.040762 | 1.2664e-14 | 1.0611e-139
Chart: T₂ (s)
| 10⁻³ | 10⁻² | 10⁻¹ | 10⁰ | 10¹ | 10²
Simulated | 0.041145 | 0.20999 | 0.94009 | 0.2963 | 0.31179 | 0.0428
Experimental | 0.040195 | 0.10657 | 0.85106 | 0.47875 | 0.3161 | 0.042802
Simulated
Experimental
Solid-fluid boundary
Water-air boundary
Geometry → M(x,t) → S(t) → f(T₂)
representative-slice approximation — not a full 3D solve

## Slide 2
Full Physical Model
Current T₂ Solver
m = [mₓ, mᵧ, m_z]T
RF pulse
solid
water
air
homogeneous field
+
post-excitation
∂M/∂t = D∇²M − M/T₂B
solid–fluid
Robin relaxation
D∂ₙM + ρₛM = 0
water–air
zero flux
D∂ₙM = 0
M(x,0) = 1

## Slide 3
CT Geometry → FEM Domain
contiguous porosity groups: max(ϕ) − min(ϕ) ≤ 0.01
3D CT stack
Representative 2D slice
Interface classification
Boundary-refined mesh
solid–fluid edge
water–air edge
water
solid
air
Ωw = water-occupied domain

## Slide 4
Magnetization Evolution → NMR Decay
↝
diffusion
↑
bulk relaxation
↓↓↓
surface relaxation
t₀
t₁
t₂
Chart: t
| 10⁻³ | 10⁻² | 10⁻¹ | 10⁰ | 10¹ | 10²
normalized decay | 0.99681 | 0.96851 | 0.72615 | 0.040762 | 1.2664e-14 | 1.0611e-139
S(t) =
∫
Ωw
M(x,t) dΩ
(M + Δt DK + Δt M/T₂B + Δt ρₛRₛ) mⁿ⁺¹ = M mⁿ

## Slide 5
Representative Slices → T₂ Spectrum
Porosity groups
Representative decays
Weighted decay
NNLS / L-curve
Chart: t (ms)
| 10⁻¹ | 10⁰ | 10¹ | 10²
Sg1 | 1 | 0.98 | 0.32 | 0.03
weight w₁
(N₁ slices)
Chart: t (ms)
| 10⁻¹ | 10⁰ | 10¹ | 10²
Sg2 | 1 | 0.98 | 0.29 | 0.03
weight w₂
(N₂ slices)
Chart: t (ms)
| 10⁻¹ | 10⁰ | 10¹ | 10²
Sg3 | 1 | 0.98 | 0.26 | 0.03
weight w₃
(N₃ slices)
Chart: t (ms)
| 10⁻¹ | 10⁰ | 10¹ | 10²
S̄(t) | 1 | 0.96 | 0.36 | 0.04
Chart: T₂ (ms)
| 10⁻² | 10⁻¹ | 10⁰ | 10¹ | 10² | 10³
Simulation | 1.0002e-05 | 1.0072e-05 | 1.1591e-05 | 3.4328e-05 | 0.00026859 | 0.0019208 | 0.0098245 | 0.035054 | 0.086991 | 0.15009 | 0.18001 | 0.15009 | 0.086991 | 0.035054 | 0.0098264 | 0.0019487 | 0.00047487 | 0.00077085 | 0.0012824 | 0.0010696 | 0.00043687 | 9.3106e-05 | 1.7818e-05 | 1.0355e-05 | 1.0008e-05 | 1e-05
Experiment | 1.001e-05 | 1.026e-05 | 1.4948e-05 | 7.5412e-05 | 0.00061118 | 0.0038508 | 0.017068 | 0.052671 | 0.11302 | 0.16861 | 0.17485 | 0.12605 | 0.063171 | 0.022012 | 0.0053438 | 0.00097465 | 0.00048944 | 0.0010182 | 0.0012999 | 0.00081371 | 0.00025207 | 4.5231e-05 | 1.2478e-05 | 1.0084e-05 | 1.0001e-05 | 1e-05
Simulation
Experiment
2D representative-slice approximation — not a full 3D solve
S̄(t) = Σg wg Sg(t) / Σg wg
min
f ≥ 0
‖Kf − s‖² + α²‖Lf‖²